IOP-MANFO-580706021

5.8GHz 7dBi Mobile Car Dome Antenna

| Electrical Specification |
| --- |
| Frequency range | 5725MHz – 5875MHz |
| Gain | 7dBi |
| VSWR | 1.5: 1 Max. |
| Polarization | Linear, Vertical |
| HPBW / Horizontal | 60° |
| HPBW / Vertical | 21° |
| Standard compliance | N / A |
| Front to back ratio | N / A |
| Isolation | N / A |
| Impedance | 50 Ohms |
| Cable | N / A |
| Connector | N Jack |
| Power handing | 20W (cw) |
| Lightning protection | N / A |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +80℃ |
| Humidity | 95% @ 55℃ |
| Radome color | White |
| Radome material | PC, UV resistant |
| Weight | 980g |
| Dimensions | 200 x 118 x 90 mm |
| Waterproof | IP-X5 |
| Shock & Vibration | EN61373, Class B, used on rolling stock |
| Mounting kit | N / A |

*Using a 50*50 cm2 flat ground plane